## Slide 1
产品描述：
产品描述:
Features
EssentialⅠ All In One
High Efficient components, Authentic materials
- LiFePO₄ battery, safe and reliable
- Highly quality monocrystalline solar panel
- Aluminum housing, robust and durable
- Easy access to battery compartment
- Protection grade is IP65 / IK08 (solar panel IK07)
- Post top and side entry with φ60 spigot
Professional light distribution, Full nominal
- Highly efficient with 150-160lm/W
- Lumen packages from 2000lm to 4500lm
- Adjustable LED module optional
- ±70° luminaire mounting angles adjustable
Intelligent dimming, High brightness and long battery life
- Intelligent charge and discharge management, 365 day light
- The working mode can be reconfigured through the remote control
- Optional combination with motion sensor for longer working hours
- 3 years warranty

## Slide 2
Product Parameters:
Product Model | UNI-SLEO-02000 | UNI-SLEO-03000 | UNI-SLEO-04500
Luminous Flux (lm) | 2000 | 3000 | 4500
System Voltage | 3.2V |  | 
Monocrystalline Solar Panel | 25W/5V | 40W/5V | 80W/6V
LiFePO₄ Battery | 3.2V/20AH | 3.2V/30AH | 3.2V/60AH
Charge Time (H) | 3~5 | 3~5 | 3~5
Full Power Working Time (H) | 5 | 5 | 5
System Power (W) | 12.5 | 19 | 30
Control Mode | Remote /Time/Optical /Intelligent Power Reduction |  | 
LED Life Time | >50,000 Hrs（L70@Ta=25℃） |  | 
Luminaire Efficacy (Tq=25℃) | 150lm/W~160lm/W |  | 
Default Lighting Mode* | 1H*100%+2H*60%+2H*30%+7H*15% |  | 
Overcast Days | 365 days lights (4-5 hours of sunlight) |  | 
CCT | 3000K/4000K/5000K/5700K/6500K |  | 
SDCM | ≤5 |  | 
CRI | Ra≥70 |  | 
Light Distribution | Batwing Light Distribution |  | 
Charge Temperature | 0℃ ~ 55 ℃ |  | 
Discharge Temperature | -10℃ ~ 55 ℃ |  | 
Storage Temperature | 0℃~ 45℃ |  | 
Warranty | 3years |  | 
Housing Materials | Aluminum Housing + Extruded Aluminum Frame + PC |  | 
IP/IK | IP65 / IK08 (solar panel IK07) |  | 
Insulation Class | Class Ⅲ |  | 
Spigot Diameter (mm) | Φ60 |  | 
Installation Height (m) | 4-6 |  | 
Luminaire Dimension (mm) | 686x351x175 | 1081x351x175 | 1231x351x175
Luminaire Packing Dimension (mm) | 805*370*125 | 1100*370*125 | 1285*370*125
Net Weight (±0.3kg) | 7.6 | 10.0 | 12.0
Gross Weight (±0.3kg) | 8.9 | 11.4 | 13.5
*Factory default value, the lighting mode can be customized as per specific requirements.

## Slide 3
Luminaire Dimension:
Model No. | Dimension（mm） |  |  | 
 | L | W | H | H1
UNI-SLEO-02000 | 686 | 351 | 175 | 45
UNI-SLEO-03000 | 1081 | 351 | 175 | 45
UNI-SLEO-04500 | 1231 | 351 | 175 | 45

## Slide 4
Note: The pictures are only the references of typical light distribution type, and the specific parameters shall be subject to the actual IES of the product.
曲线配光：
Light Distributions:
Type II

## Slide 5
Maintenance:
To ensure the solar panels can receive light effectively, please clean the surface of the solar panels with a soft cloth and water regularly. Do not use chemicals and abrasives that containing strong solubility such as ammonia.
Recommended storage time shall be less than 3 months as the battery will be affected by self-discharge. If it has been transported or stored for a long time, please check, charge and make record regularly, otherwise it will affect the capacity and service life of the battery.
Make sure installing the solar panel face to the direction where has most sunlight, so that it can effectively absorb the sunlight energy. Avoid tall buildings or trees that may block the sunlight, and places with heavy dust need to be cleaned up in time.
All screws shall be tightened evenly according to the standard, and should not be loosened and shaken.
Cautions:
Solar panels belongs to “fragile” product category. Please do not scratch or apply impact on panel during installation, as the scratches, dust, and occlusion on the surface will affect the efficiency of power generation of solar panels.
Solar panels facing south for places in the northern hemisphere, and facing north in the southern hemisphere.
Before installation and use, please refer to this manual for faster and more accurate use of this product.
Before installing and using this product, it is necessary to ensure that the lamp body is intact and free from defects from the appearance
If there are any problems during installation, please contact professional technical personnel first before proceeding with normal operations.
The lamp body lighting operates independently, and automatically activates the built-in intelligent mode for operation when the switch is turned on.

## Slide 6
When the product is not in use, it shall be charged every 3 months. If long-term transportation or storage is required, it shall be checked, charged and recorded in time, otherwise battery life may be affected. Charging method: under a sufficient sunlight, turn on the lamp, turn the solar panel facing to the sun, charge continuously for 1-2 days, read the status with the remote control that display it is in charging.
The installation of lamps should be away from WIFI, omnidirectional antennas for mobile communications, small base stations for telecommunications, and TV antennas. Signal sources that are too close may disable the dimming function.
The lamp should not be installed on the vibrating surface, and the shaking of the lamp may cause the sensor to be triggered by mistake.
The dimming function of the lamp may be affected by the presence of vibrating objects in its sensing area.
The microwave sensor has a good penetration performance though plastic and wood. Please avoid metal shielding around, which will reflect and block microwaves, affecting the actual induction performance.
Walls, glass, ceramics will bring microwave reflection and penetration attenuation, reduce the sensing distance of the sensor, the thicker the material, the more serious the attenuation.
In the actual application environment, the sensing range of microwave sensors will be different due to the different reflectivity of obstacles.
If there is a glass barrier between the infrared sensor and the detection object, and the far infrared ray passing through in it, while the heat source in the detection range is almost not moving or moving at high speed, sensor may not be triggered.
The movement of animals and objects within the sensing range may cause false triggering, causing the light to turn on.
Microwave sensor is not suitable for lakes, rivers, seaside and similar places.
Turn on the switch of the lamp before use. Before installation, test whether the lamp is able to charge and discharge (the solar panel is charging under the sunlight and the lights are off. Solar panels is discharging when panel is fully blocked and lights are on).
Do not put the lamp in water or fire, there may be a risk of explosion.
This product can withstand hurricanes of Category 14, hurricanes higher than Category 14 may cause damage to the product.

## Slide 7
HQ Address: 112 Yongfu Rd., Qiaotou Village, Fuyong Town, Baoan District, Shenzhen 518103 China.
Manufacturing Base: Unilumin Industrial Park, 6th Lanjing North Road, Pingshan District, Shenzhen, China.
TEL：+86-0755-29918999
FAX：+86-0755-29912092
www.unilumin.com
www.unilumin-lighting.com
Maintenance/teardown shall be conducted by professional or technical personnel. For the lamps are no longer in service, the battery needs to be taken out by professionals too.
If there is a need for change of light source in this lamp, it should be replaced by the manufacturer or its service agent or a similarly qualified person.
The product contains lithium batteries, which is regarded as flammable and explosive materials. Please abide by the air transportation regulations during transportation: do not fall violently and lift the package gently during transportation. Storage should be separated from other items to avoid damage.
When the continuous rainy days are longer than the design days, the battery power will be drained. Due to the extremely low charging efficiency in rainy days, you may see the working time is short, this is normal. The working time will improve when the sunny days is back.
Product specifications are subject to change without notice, and the final interpretation right of this specification belongs to the manufacturer.